## Slide 1: WebCT
Fully Featured Browser-Based Interactive X-Ray Simulations for Scan Planning and Training
Mr Iwan T. Mitchell1, Dr Franck Vidal1, Dr Llion Evans2, Dr Simon Middleburgh1, Mr Fabio Martini1, Mr Gareth Stephens1
1 School of Computer Science & Electronic Engineering, Bangor University
2 Collage of Engineering, Swansea University

## Slide 2: X-Ray Simulation
X-Ray simulation is increasing in popularity with the push towards digital twinning, component testing and machine learning.
Simulated results can answer feasibility questions without requiring beam time. Can you scan this component on your setup? What is the best tube voltage? Etc.
Monte-Carlo methods are highly accurate physically-based approaches, but take a very long time for even a single projection (more than hours on a supercomputer)
  This is a very large bottleneck

## Slide 3: GPU-Accelerated Simulations
Raytracing is an approach to X-Ray simulation that does not take into account scattering.
Raytracing on CPU is quite slow…
  … But GPUs are built for parallelism and are super fast!
gVirtualXRay is an open-source library that is able to provide realtime simulated X-Ray rendering with no cost.
gVXR supports a wide range of languages for its C++ API, including python.
  This makes gVXR easily scriptable and integrated alongside popular data analysis toolsets.

## Slide 4: Digital X-Ray Ecosystem
ASTRA Tomography Toolbox
CT Reconstruction Libraries
TIGRE GPU Reconstruction Library
Beam Spectra Generation
Xpecgen
Spekpy
Fast X-Ray Simulation

## Slide 5: WebCT: What is it?
WebCT: “Interactive Web UI for X-ray CT with Real-Time Results”
WebCT provides an easy-to-learn User Interface for simulated X-Ray capture to reconstruction.
Aims to provide a fully-featured experience while not being complex for those new to X-Ray tomography.
An open-source useful tool for scan planning and training.
… Why talk about it, when you can show it?

## Slide 6: Fuel Pellet Case Study
Nuclear fuel must adhere to strict standards to ensure a safe operation within a reactor.
  We can use X-ray CT to inspect pellets, but a high X-ray opacity of uranium makes scanning challenging.
The use of ZrO2 as a surrogate material is quite popular to replicate the behaviour of UO2 dust during manufacturing.
Both real and surrogate pellets contain ZrB2 ceramic kernels we want to detect automatically, but the outer material attenuates more than the pellets.
However…
  We have no experience in X-raying surrogate pellets
  We don’t know what power we would require
  We don’t know what detector resolution is needed
  Etc…

## Slide 7: User Interface
Section Tabs
Section
Parameters
Global preview pane
Section Pane

## Slide 8: Beam Source
Source type and generator
Anode parameters
Filter
X-Ray Spectra Graph

## Slide 9: X-Ray Detector
Resizing Detector Visualisation
LSF Editor
Resizing Detector Visualisation
Live Size Preview
Resizing Detector Visualisation

## Slide 10: Samples and Materials
Sample cards
Material Library
Mixture editor
Categories and Materials

## Slide 11: Capture Plan
Geometry Diagram
Animated capture preview
Free axis translation of source and detector
Nyquist projection count slider

## Slide 12: Reconstruction
Animated reconstruction preview
Support for many different reconstruction methods
All parameters exposed for even iterative methods

## Slide 13: Case Study Results
Simulated Surrogate Sample | Real Scan at Diamond

## Slide 14: Case Study Results
Simulated Surrogate Sample | Real Scan at Diamond
Not a kernel
Resultant grey value much smaller than expected assumedly due to powder compaction

## Slide 15: Accessible Configuration
WebCT aims to fit a specific task and understands it can’t do everything.
All the configuration settings are exportable into WebCT’s JSON format, and even GVXR JSON format for use with your own python applications.
  Reproducible and shareable environments!
  This makes WebCT powerful, interactively setup your scan geometry with WebCT, and use a simple python script to simulate hundreds of samples…
WebCT also supports importing other system’s configurations.
  We can load in a GVXR setup, and support for other scanning metadata formats (XTEK, etc) is coming soon!

## Slide 16: Open Source
Development all open on Github
https://webct.io

## Slide 17: Thanks for Listening